## Slide 1: DARA Unit 2-3 Lectures Radio Frequency Interference
VenKATasubramani Lakshmanan Thondikulam
Sr. Engineer (Retd), GMRT-NCRA-TIFR, India
Project Manager – AVN (Retd), SARAO, South Africa
venkatska@gmail.com +91 89711 11881
GRAO, GHANA June 3, 2021

## Slide 2: Growing up at ORT and OSRT… 1974-84

## Slide 3: Mid career…. GMRT and OSMA 1985-2007

## Slide 4: The Finale: KAT-7, MeerKAT & AVN 2008-17
Currently, quality time with family in India; Involved in setting up 3 Geodetic VLBI stations in India; DARA support etc.

## Slide 5: Plan
The Electromagnetic Spectrum – A Primary Resource in Communication
Interference and Types of Interference
Few anecdotes on RFI in radio astronomy observatories
Mitigation Measures – in domains other then DSP
Over to Nadeem, to talk on Mitigation Measures in Data Processing

## Slide 6: The Electromagnetic Spectrum and Radio Astronomy
A Radio Telescope is NO DIFFERENT from any other communication receiver you know of like cellphone, television etc, EXCEPT that the Transmitter here is FAAAAAAR away and radiates electromagnetic waves by NATURAL phenomenon.
The Radio Telescope System processes and records the VERY SMALL perturbation in the background noise as received from a celestial object in the field of view of the antenna
The recorded signal with an accurate time stamp is used for studies towards interpretation of the physics of the object and thus lead towards advancement of our knowledge in the fields of astronomy, astrophysics and cosmology through techniques of radiometry, spectroscopy and accurate timing
The document https://www.itu.int/rec/R-REC-RA.314-10-200306-I/en lists the preferred frequency bands for radio astronomical measurements
THUS, THERE IS A WIDE RANGE OF FREQUENCIES USED BY RADIO ASTTRONOMY COMMUNITY AROUND THE WORLD. HOWEVER, ONLY A SMALL SUB-SET WILL BE OF RELEVANCE FOR A RADIO TELESCOPE. FOR EXAMPLE, GRAO IN GHANA USES:
  VLBI at 5 GHz: 4926.49 to 5054.49 MHz
  Methanol, Single Dish and VLBI: 6650 to 6685 MHz.

## Slide 7: The Electromagnetic Spectrum and ITU, NCA, ICASA etc
The International Telecommunication Union (ITU) is a specialised agency of the United Nations. It recommends and coordinates usage of the electromagnetic spectrum internationally through Radio Regulations.
ITU has recognised RADIO ASTRONOMY as one of the ~THIRTY services needing spectrum allocation
The spectrum is regulated, allocated and managed between the services nationally by National Communications Authority (NCA) in Ghana, Independent Communications Authority of South Africa (ICASA) in SA etc. They also coordinate harmonious usage across borders.
Protected chunks of spectrum from 9kHz to 300 GHz is available with a roughly octave spacing for continuum research in radio astronomy. Protected narrow chunks are also available for spectral line studies (Eg: 1610-1612.6 MHz for OH line studies).
Allocation varies as PRIMARY (exclusive/ shared), Secondary, Additional, Foot Note mention etc.

## Slide 8: Interference to Radio Telescope
Radio astronomers have set a limit of 10% loss of data owing to RFI as JUST acceptable and above 10%, unacceptable. This requirement is now incorporated by reference in the ITU Radio Regulations.
VLBI mitigates against interference because the SAME interference is not present at both sites, and does not therefore correlate. However, t does affect the measurement of system noise and hence the calibration of the system, so it is important to minimise it.
The Radio Astronomy Receiver operates over a wider range of frequencies to study red-shifted lines and the designer needs to “harden” the design to achieve a linear system in the presence of other signals
A MAJOR EFFORT OF COORDINATION WITH OTHER USERS, ACTIVELY SUPPORTED BY THE SPECTRUM REGULATOR OF A COUNTRY IS CRITICAL FOR THE SUCCESS OF ENDEAVOURS IN RADIO ASTRONOMY

## Slide 9: Types of Interference to Radio Telescope
Conducted (powerline etc) and Radiated RF (microwave oven etc)
External (cellphone etc) and Internal (self-generated – harmonics, intermodulation in receivers)
RF and Non-RF

## Slide 10: A few Anecdotes on mitigating RFI in Observatories
The Hunt for “~6 RFI Events/Day” at Ooty, India in 1977
The Oscillating LNAs at Ooty circa 1980
The TV Booster LNA improvement at a few thousand
private residences around GMRT in India
during 2000-2006

## Slide 11: A few Anecdotes on mitigating RFI in Observatories
The Sherlock Holmes of VLA – Identifying source of sporadic night time broad-band interference
Voluntary RFI prevention measures by residents of Greenbank
MeerKAT mobile Control in south Africa
RFI - Perytons

## Slide 12: RFI Mitigtion Measures
Adequate Headroom in receiver design for linearity
Care in choosing frequency of Local Oscillator signals
Shielding
Earthing, Powerline Management
Filtering
Observatory RFI discipline
Active participation National and Internatinal Spectrum management activities
Outreach to local community
RFI algorithms in data processing – Over to Nadeem

## Slide 13: QUESTIONS
An extract from Radio Regulations is shown on the left
The Three REGIONS are explained HERE.
Why has the whole World accepted to PROHIBIT
ALL EMISSIONS in 1400-1427 MHz band and allocate
This band EXCLUSIVELY for passive services similar
To Radio Astronomy?..
This experimental set-up uses 2 dish antennas each of 3m. dia pointed permanently
to zenith, separated by a distance of 50 meters. The antenna is equipped with a radio
astronomy receiver operating at 322-328.6 MHz Radio Astronomy band.
The signals from the two antennas are multiplied and the DC voltage output is recorded.
A rogue LEO (Low Earth Orbit) satellite with an orbital period of 90 minutes sweeps
across the beam of the dishes.
Please find what will be FRINGE FREQUENCY recorded.