## Slide 1: Spectral Line Data Reduction
Joe Callingham
Kenya 2018
Based on talks by Katharine Johnston (University of Leeds) and Luke Hindson

## Slide 2: Introduction
We have discussed some of the science you can do with spectral lines
In this lecture we will explore the important differences between spectral line and continuum data reduction
  Setting up your observations
  Data reduction
  Image and spectral analysis

## Slide 3: What is spectral line interferometry
Observing many adjacent frequency channels with an interferometer for an object whose flux changes rapidly with frequency
Results in a third axis: frequency or velocity
CO (6-5) emission from a high redshift quasar observed with the Plateau de Bure interferometer (Wang et al. 2010)

## Slide 4: What is spectral line interferometry
However, today even continuum observations are carried out with many channels (called pseudo continuum)
Therefore, you need to understand spectral line interferometry to do (almost all) interferometry
Plot of response across a band for one VLA antenna as a function of channel during the reduction of continuum data

## Slide 5: Setting up you observations
Choose your science case and lines(s)
choose your source(s) and research its properties
Choose your interferometer and configuration
Check source velocity reference frame, on-line Doppler tracking
Choose the channel width, total bandwidth, and number of channels
Determine your required sensitivity and time on source
Choose your calibrators
Data rate and size considerations

## Slide 6: 1. Choose your science case and line(s)
Doppler shifts → Velocity fields
Choose spectral line(s) for science case
Find which telescopes have bands that can observe the line(s)
Physical properties from lines for science case
Dynamics
Optical depth
Excitation Temperature
Density
Column density
Turbulent motions
Magnetic field strength
Chemistry
Velocity field of galaxy M33 in HI line. Colours show Doppler shift of line and brightness is proportional to HI column density (NRAO, Thilker et al.
VLA HI @ 21cm

## Slide 7: Commonly observed lines: HI line at 21cm (1.4 GHz)
Can determine:
Morphology of atomic gas
Dynamics
  gives enclose mass (inc dark matter)
column density and mass of optically thin gas
temperature of optically thick gas
distance via Hubble law

## Slide 8: Commonly observed lines: Radio Recombination Lines (RRLs)
Can determine:
Ionised gas dynamics
optical depth and electron temperature (in Local Thermodynamic Equilibrium, LTE)
Gas density from collisional broadening of the lines
Speed of turbulent motions from linewidths (for low n)
Abundance ratio of H/He/C
Magnetic field strengths from Zeeman splitting
RRLs for n=91 and 92 for H, He and C in an HII region (Quireza et al. 2006)

## Slide 9: Commonly observed lines: Molecular lines
Can determine:
Morphology of molecular gas
Dynamics
Gas column and volume density
Optical depth
Temperature
Abundances
Magnetic field strength
Chemistry
Presence of shocks (SiO)
AGB star R Sculptors
CO (J=3-2) with ALMA
Maercker et al. (2012)
Common molecular lines:
CO, OH, H2O, SiO, HCN, methanol, NH3
Can also observe absorption lines and masers.

## Slide 10: 2. Choose your source and research its properties
Learn about the object you wish to study e.g
Position (and equinox)
Size
Velocity (and reference frame)
Estimated brightness
Search for literature on your source using resources like:
ADS (http://www.adsabs.harvard.edu/)
NED (https://ned.ipac.caltech.edu/)
CDS (http://cds.u-strasbg.fr/)

## Slide 11: Choose your interferometer and configuration
Large number of possible instruments to name just a few:
  (J)VLA, ALMA, MWA, LOFAR, PdB, ATCA, EVN, AVN
Read about the telescope online e.g for the VLA

## Slide 12: 3. Choose your interferometer and configuration(s)
(J)VLA
Part of the ALMA Compact Array
Larger arrays: better resolution! Good for absorption studies as want to detect a small, bright background source
Smaller arrays: have better surface brightness sensitivity so easier to detect extended or faint emission

## Slide 13: 4. Check source velocity reference frame
Need to always specify the velocity reference frame

## Slide 14: 4. Check source velocity reference frame
Optical Barycentric or Heliocentric system often used for extragalactic observations
Radio Local Standard of Rest (LSR) used for Milky Way observations

## Slide 15: Doppler shift and Doppler Tracking
on-line Doppler tracking automatically corrects to a given reference frame during the observation in real time
The tracked or observed frequency is usually called the sky frequency
However, for wide frequency bands (most modern interferometers) on-line Doppler tracking is not done / recommended as correction is only strictly correct at one frequency
Instead Doppler Setting is used, i.e. sky frequency calculated once at the start of the observation
Further corrections can be made during the data reduction and imaging stages (need > 4 channels across the line for good correction)

## Slide 16: 5. Choose the channel width, total bandwidth and number of channels
Channel width determined by required spectral resolution and sensitivity
Total bandwidth should:
  Leave good line free channels at the ends of the band for continuum subtraction (end channels often bad)
In a “lag” correlation, total number of channels is conserved, so total bandwidth is directly related to channel width

## Slide 17: Velocity Coverage
For radio/millimetre frequency observations:
Where Δf is the bandwidth (Hz), f the rest frequency (Hz), Δv is the velocity span (kms-1) and c = 3 x 105 kms-1, the speed of light
So if you want a velocity coverage of 100 kms-1 at a frequency of 22.2 GHz then:
Allow some leeway for filter edge effects.

## Slide 18: Velocity Resolution
It is good practice to have a velocity resolution with at least 3 channels between the half power points of a typical spectral line
So if you have lines with typical FWHM of 1 km/s at 22.2 GHz then you want a spectral resolution of:
Many correlates have a maximum channel bandwidth product. Often you want to select the configuration with maximum bandwidth for the required velocity resolution

## Slide 19: Gibbs Ringing and Hanning Smoothing
Hanning Smoothing
Smooth data with a running mean in frequency with weightsL
  0.5 for central channels
  0.25 for adjacent channels
  i.e a triangular smoothing kernel
Pro: reduce ringing
Con: reduces spectral resolution by 2
Seen at channel edges
Also see for bright lines e.g masers, RFI
Gibbs Ringing
Fixed by

## Slide 20: 6. Determine your required channel sensitivity and time on source
Determine how many channels needed to adequately resolve your line (e.g. >5)
If detection is important, need to detect line peak channel with >3-5 sigma
If need to resolve emission in different channels for e.g. dynamics, need to detect line in faintest of these channels with >3-5 sigma
You should determine the estimated flux of the source (May need to convert from brightness temperature Tb or expected column density)
Use sensitivity calculator to determine required time on-source (e.g. VLA, ALMA, SMA, ATCA)

## Slide 21: 7. Choose your calibrators   Bandpass calibration
The bandpass is the spectral frequency response of an antenna to spectrally flat source of unit amplitude
Phase
Amp
0
10
20
-20
-10
1.0
0.8
0.6
0.4
0.2
0.0
1.2
0
10
20
-20
-10
1.0
0.8
0.6
0.4
0.2
0.0
1.2
Ideal Bandpass
Phase = 0, Amp = 1
Observed Bandpass
The observed phase and amplitude is not ideal because of delay error and limitation of the antenna transmission and electronics

## Slide 22: Why is bandpass calibration important?
The quality of the bandpass calibration is a key limiting factor in the ability to detect and analyse spectral features
v-dependant amplitude errors:
  limit ability to detect/measure weak emission/absorption lines superposed on the continuum
  may mimic changes in structure
v-dependant phase errors:
  may lead to spurious positional offsets between spectral features as a function of frequency, imitating Doppler motions
    Relative positional accuracy in channel images where is the synthesised beam and is the scatter in the phase
  For pseudo-continuum experiments conducted in spectral line mode, dynamic range of final images is limited by bandpass quality

## Slide 23: What makes a good bandpass calibrator?
Select a bright continuum source with:
High SNR in each channel
Intrinsically flat spectrum
No spectral lines/features
No changes in structure across band (e.g. point source at all frequencies
Calibration should not contribute to noise in target spectrum, i.e. in one channel:
bandpass SNR > target SNR
Can smooth the bandpass or fit polynomial to increase the SNR
May need a higher SNR for bandpass calibrator if looking for faint lines on strong continuum

## Slide 24: 7. Choose your calibrators Flux calibration
In mm/sub-mm observing, if using solar system object with an atmosphere for calibration (Jovian or Saturnian moons, for example), be aware that these objects often have absorption lines
Check your calibrator spectrum carefully, particularly if that source is not red-shifted
You should exclude affected channels (or even baseboards if the absorption is broad)
Titan clearly shows multiple emission features

## Slide 25: 8. Data rate and size considerations
Finally, many observatories impose a maximum data rate for a given observation
For instance, for the VLA the data rate depends on:
  The number of channels
  The number of spectral windows
  The number of polarisations observed
  The length of one integration in seconds
  the number of antennas
  It is not uncommon for datasets to be in the many 100s of GBs. Large datasets are difficult to transfer and reduce…. only use high spectral and time resolution if you really need it.

## Slide 26: Data reduction
Flagging methods
Bandpass calibration
Doppler correction
Continuum subtraction
Self-calibration
Imaging of cubes

## Slide 27: Flaggin Methods - in frequency
For large data sets, checking the data channel-by channel is not practical
This task can be simplified using approaches such as:
  Examination of scalar-averaged cross-power spectra: check for dips or spikes
  Use of automated flagging routines: these can flag based on deviation from expected spectral behaviour (e.g. SERPent, for e-MERLIN, AOFlagger)
But… if you are planning to make image cubes then avoid excessive frequency dependant flagging which changes the uv-coverage across the band

## Slide 28: Bandpass calibration
Has your bandpass calibration gone well?
Examples of good-quality bandpass solutions for 2 antenna
Solutions should look comparable for all antennas
Mean amplitude ~1 across useable portion of the band
No sharp variations in the amplitude and phase
Variations are not dominated by noise

## Slide 29: Bandpass calibration
Another good way to check: examine cross-power spectra of a continuum (flat spectrum) source with BP corrections applied
Checklist:
  Phases are flat across the band
  Amplitude is constant across the band
  Corrected data do not have significantly increased noise
  absolute flux level is not biased high or low

## Slide 30: Bandpass calibration
When has your bandpass calibration gone bad?
The solutions shown are clearly bad
Problems:
Amplitude different normalisation for different antennas
Noise levels are high, and are different for different antennas

## Slide 31: Doppler correction
Often now done using Doppler Setting and further finer corrections during post-processing and imaging
Within one observation, Doppler Setting can correct for the Heliocentric velocity (~30 km/s), but cannot exactly correct for the ~0.5 km/s for the Earth’s rotation on its axis
Remaining corrections done in e.g. tasks clean or cover in CASA and task CVEL in AIPS (after bandpass calibration). CASA task plots can correct on-the-fly (less accurately).
Different colours are different times in the observations
Before
After

## Slide 32: Continuum subtraction
As well as lines, spectral-line data often contains continuum sources (either from the target or from nearby sources in the field)
  This emission complicates the detection and analysis of line data
  Continuum emission limits the achievable spectral dynamic range
Spectral line cube with two continuum sources (structure independent of frequency) and one spectral line source near the field centre Roelfsma(1989)

## Slide 33: Continuum subtraction
Method:
examine the data
assess which channels appear to be line-free
use line-free channels to estimate the continuum level
subtract the continuum
evaluate the results

## Slide 34: Continuum subtraction: Two methods
In the uv-plane
  subtract continuum then clean line & continuum separately
    Use AIPS tasks such as UVLIN, UVLSF, UVSUB
    Use CASA tasks such as uvcontsub
In the image-plane
  FT data, subtract continuum from the “dirty” cube then clean both continuum & line
  Use AIPS task such as IMLIN
  Use CASA tasks such as imcontsub
No one single subtraction method is appropriate for all experiments!

## Slide 35: Self-calibration
Can apply self-calibration solutions to improve quality of line data
Two cases:
Strong line emission (i.e. maser)
  Choose a strong channel with “simple” structure
  Self-cal that channel & apply solutions to all other channels
  Allows imaging of weak continuum (& channels) with improved SNR
Weak line and strong continuum emission
  Apply solutions from the continuum to individual channels
  Allows imaging of weak lines with improved SNR
Get good positions of line features relative to continuum, but lose absolute positional information

## Slide 36: Imaging of cubes
Principles for continuum imaging mostly apply to line data as well (cleaning, weighting, etc.)
But keep in mind that deconvolution of spectral line data often poses special challenges:
  Cleaning many channels is computationally expensive (do you need the full spectral resolution or can you average?)
  Emission structure changes from channel to channel (may have to change cleaning boxes for each channel)
  If you are interested in both high sensitivity (to detect faint emission) and high spatial/spectral resolution (to study kinematics):
    robust weighting with -1<R<1 good compromise

## Slide 37: Image and Spectral Analysis
After mapping all channels in the data set, we have a spectral line 3D data cube (RA, Dec, Vel or Freq)
To visualise the information we usually make 1-D or 2-D projections providing differing analysis methods:
  Line profiles (1-D slices along velocity axis)
  Channel maps (2-D slices along velocity axis)
  Moment maps (integration along the velocity axis)
  Position-velocity (PV) plots (slices along spatial dimension)
  Movies (2-D slices along velocity axis)

## Slide 38: Line profiles
Spectra taken from three different positions in the 13CO (J=1-0) G305 cube.
Used KVIS to output the ascii data for each spectra then made into an image using Python

## Slide 39: Channel maps
Channel maps of 12CO (J=1-0) towards G305
Steps through channels from -57 km/s to -1 km/s
Integrates emission over 4 km/s

## Slide 40: Moment maps
Moment maps can be used to derive parameters such as integrated line intensity, centred velocity and line widths as a function of position
Total intensity (moment 0)
Intensity-weighted velocity (moment 1)
Intensity-weighted velocity dispersion (moment 2)
These maps can be made with AIPS tasks like MOMNT, CASA’s immoments or Miriads moment

## Slide 41: Moment maps
moment 0
moment 1
moment 2
Moment maps are sensitive to noise so clipping is required
Sum only over the planes of the data cube that contain emission
Since higher order moments depend on lower ones (so progressively noise), set a conservative intensity threshold for the 1st and 2nd moments

## Slide 42: Position-Velocity (PV) diagrams
PV diagrams take a slice out of a cube along a “PV cut”
You can produce PV diagrams in CASA using task impv, or IMMOMENTS
This PV diagram was created in kpvslice
Try exploring the CO cubes to see if you can spot any interesting velocity structures
  Edges of molecular clouds?
  Star forming regions?