## Slide 1: Introduction to EVN data
Joe Callingham (ASTRON)
Kenyan Radio Astronomy School,
Nairobi, Kenya
29th of May 2018

## Slide 2: VLBI
EVN made of

## Slide 3: EVN
Ad-hoc array of about ten regular members (can be up to
Largest regular member 100-m Effelsberg. Smallest <20m
Phased arrays e.g. WSRT also have large effective areas

## Slide 4: Data Transport
Most data recorded at each telescope onto computer disk packs (originally, tapes)
  Shipped to JIVE correlator, The Netherlands
Now it is possible to get all the data over the internet in select cases

## Slide 5: Notes of warning!
The EVN has great collecting area for a VLBI instrument but it is an ad hoc array
You have to reconnect the puzzle in just the right way (especially for polarization)

## Slide 6: The observations – n14c3
Observed (gain calibrator, phase calibrator, and source) 2014 Oct 22 in C-band (~5 GHz)
Sweet spot for VLBI as receivers are sensitive, sky noise is low, and limited impact from atmosphere

## Slide 7: (Simple) Calibration Strategy
Observe bright source with known flux density for gain calibration
Go to phase calibrator (reasonably bright – usually ~100 mJy at least)
Go to source (which might be too faint to observe in real time)
Back to phase calibrator (time set by frequency, observing conditions, etc)
Repeat 3 and 4 until reach desired noise floor
Usually finish on Gain cal.

## Slide 8: Remember all telescopes need to see sources!

## Slide 9: Observations
12 antennas used
Data recorded on disc
Data correlated at JIVE and stored in FITS IDI format
Tsys measurements recorded separately
  Gain elevation curves also recorded

## Slide 10: Summary of observation status

## Slide 11: Calibration is to fix this mess…

## Slide 12: Delay (phase v. frequency)
Correlated data have residual timing errors
These data are pretty good!
Very important to correct before averaging (otherwise decorrelate)

## Slide 13: Manual processing of n14c3

## Slide 14: Manual processing of n14c3

## Slide 15: Manual processing of n14c3

## Slide 16: The result
Thanks to Anita
n14c3 image of 3C345